## Slide 1
Problem Statement ID – [ Enter PS ID ]
Problem Statement Title – Automated Road Obstruction & Hazard Mapping from Street/Dashcam Video
Team Name – Team UniVerse
Team Leader Name – [ Enter team leader name ]
Members Names – [ Enter member names ]
Our solution

## Slide 2: IDEA TITLE: TerraTrace
Proposed solution: dashcams become hazard sensors; every hazard becomes a tracked case.
1 Camera sees the road
Helmet/dash camera on NH3, Himachal
2 AI spots the hazard
Water across the road: flooding, 96%
3 Mapped & tracked
Route, exact pins, case for the department
Sees what satellites miss
Floods, landslides, fallen trees, potholes under canopies & overpasses
Exact hazard location
Camera geometry pins the hazard itself, not just the car
Detection → resolution
Each hazard is a case: priority, department, deadline, status

## Slide 3: TECHNICAL APPROACH
How it works, in five steps
1. Capture
Phone or dashcam video with GPS
MP4 + GPX
2. Detect
AI finds potholes, cracks, floods, landslides
YOLOv8 + CLIP
3. Locate
Camera angle + GPS → exact map point
Geometry + GPS
4. Map
Live map, routes, closures & detours
Leaflet + GeoJSON
5. Act
Case per hazard, routed to a department
Case workflow
Built with
Python
YOLOv8
YOLO-World
CLIP
OpenCV
FastAPI
SQLite
Leaflet
GeoJSON
Runs on a laptop GPU (Apple M5): no cloud needed. Three ways in: upload a drive, replay it live, or stream a phone camera.

## Slide 4: TECHNICAL APPROACH — WORKING PROTOTYPE
TerraTrace Home: an animated tour draws every analysed route from start to end and drops hazard pins as it passes them.
22 fps
AI speed on a laptop GPU
4×
faster than real time
3
inputs: upload · live replay · phone
16/16
test checks on 3 real clips
Evidence photo saved with every hazard

## Slide 5: TECHNICAL APPROACH — PLATFORM
From detection to resolution: one platform for the control room
Case tracking
Detected → target fix, priority, department, evidence, notes
Workflow board
New → Verified → Assigned → In progress → Resolved
Command
AI-view video synced with the map; live alerts & detours
Also: one-click incident report (PDF) for authorities · road health grade per drive · GeoJSON / CSV export for any GIS · phone-as-dashcam live mode

## Slide 6: FEASIBILITY AND VIABILITY
Feasibility analysis
Already working end-to-end
Upload, live replay & phone streaming → mapped cases with a full workflow
No special hardware
Runs on a laptop GPU; any phone or dashcam is the sensor
Open data & models
Pretrained on RDD2022 (47k+ images); open-source stack, no licence cost
Challenges & risks → our strategies
Challenge / risk | Strategy
AI misses or invents hazards | Whole-road CLIP scene check finds floods & landslides; dry roads and hillsides are filtered out; fine-tune next
Intermittent / noisy GPS | Time interpolation + heading smoothing; GPS-gap flag on every hazard
Unknown camera mounting | Camera presets (phone / dashcam / helmet) + automatic tilt from the horizon
Same hazard seen many times | Object tracking + spatial clustering → one case per real hazard
Phone can't reach the laptop | Single HTTPS server; phone hotspot fallback

## Slide 7: IMPACT AND BENEFITS
Municipal corporations
Pothole & road-damage inventory from buses, garbage trucks, taxis; repairs prioritised and tracked to closure
Disaster response teams
Within hours of a storm or landslide: which roads are blocked or flooded, and the detour around them
Citizens & commuters
Safer routing, fewer accidents and vehicle damage; transparent public hazard map
Key benefits
Low cost — reuses phones & dashcams already on the road
Fast — hazard map in minutes, not days of surveys
Accountable — every hazard has an owner, a deadline and a status
Interoperable — standard GeoJSON for any GIS or city dashboard
Tested on an Indian highway (NH3, Rohtang): flooding detected, road closed, detour found

## Slide 8: RESEARCH AND REFERENCES
1
RDD2022 road damage dataset
Arya et al., arXiv:2209.08538 · github.com/sekilab/RoadDamageDetector
2
comma2k19 driving dataset (video + GNSS)
github.com/commaai/comma2k19
3
YOLOv8 / YOLO-World (Ultralytics)
docs.ultralytics.com · Cheng et al., CVPR 2024
4
RDD-trained YOLOv8s weights
github.com/oracl4/RoadDamageDetection
5
CLIP: zero-shot image–text matching
Radford et al., ICML 2021 · github.com/openai/CLIP
6
ByteTrack multi-object tracking
Zhang et al., ECCV 2022
7
DBSCAN density clustering
Ester et al., KDD 1996
8
GeoJSON · Leaflet · OpenStreetMap
IETF RFC 7946 · leafletjs.com · openstreetmap.org
9
OSRM routing · Nominatim geocoding
project-osrm.org · nominatim.org (detours, place names)
10
TerraTrace source code
github.com/aryan270506/Team-UniVerse-Geo-AI
11
Indian road footage (NH3 demo)
KSOFTECH, CC BY 3.0, via Wikimedia Commons